IKS-Cluster autoscaler with kubernetes tainting
Agenda:
    1- Problem
    2- Solutions and User steps
    3- IKS-CA tests and results
    4- Tainting problem, impacted components and solutions
    5- Demo
    6- Questions/Discussion/Suggestions??
IKS Cluster Autoscaling Team

---
Problem:
As of IKS-CA can’t scale down any worker pool to 1 because of system or local storage pods
like ALB, calico, calico-typha etc
Solution:
User can taint the worker pool(apart from default WP) and then enable that worker pools for
scaling but deployed PODs on those worker pool should add the toleration.
Step 1- Select the worker pools which needs to be enabled for cluster autoscaler
Step 2- Taint these worker pools by using `ibmcloud ks` cli either same or different-2 taint values, worker pool will only accept
        matching or wildcard toleration pods
Step 3- Enable these worker pools with cluster autoscaler
Step 4- Add toleration in the functional PODs accordingly, like if user want to deploy a apps/pods
        per worker pools then they may have different-2 taints for each worker pool.
Is this working as expected?
Yes, able to scale down worker pool to 1

---
IKS-CA testing results with tainting:
a- Cluster with 1 worker node in default worker pool and scale different pool with same zone:
Why?: To test ALB(which need 2 nodes) and other such components
Result/Observation: 2/3 system pods are in pending state always, able to scale down to 1
b- Cluster with 2 worker node in default worker pool and scale different pool with same zone:
Why?: To test success case of ALB and other such pods
Result/Observation: Worked fine and able to scale down to 1
c- Cluster with 2 zones(1 node each) in default worker pool and scale WP with different zone:
Why?: To test ALB and storage
Result/Observation: Worked fine and able to scale down enabled WP to 1, pods which need to run in all zone were always be in pending state like public-crbr1u25hw05el16h9vrmg-alb1
d- Cluster with 1 zones in default worker pool and scale WP with different zone:
Why?: To test ALB and storage
Result/Observation: Worked fine and able to scale down enabled WP to 1, pods which need to run in all zone were always be in pending state like public-crbr1u25hw05el16h9vrmg-alb1, Tried to exec to functional pod which was deployed on the WP which was enabled and exec worked fine.

---
Problems with tainting:
As tainted node will allow only those work loads which matches their toleration hence
those iks components which require to run either on each worker pool, zone, or at each node level
will not run because of taints. Following are the know components which will be impacted
1- Storage vpc-csi driver for node server
2- Block storage daemon set
3- calico-node
4- ibm-master-proxy-static
5- public-*-alb1
6- any other ???
Solution:
        If we want to deploy above or other components to each nodes or worker pools then these components should have toleration matching with worker pool taint.
Better option to have wildcard global toleration on all impacted IKS components.
Need following changes to all such components in `pod` section of deployment files
spec:
      tolerations:
      - operator: Exists
      containers:

---
Error from POD which will not tolerate:
 Warning FailedScheduling 34s (x11 over 10m) default-scheduler 0/5 nodes are available: 1 node(s) had taints that the pod didn't tolerate, 4 node(s) didn't match node selector.

---
Demo:
1- How to taint WP and check the tainting
-Imputes: Cluster, Worker pool, taint key and value
curl -X POST "https://us-east.containers.cloud.ibm.com/v2/setWorkerPoolTaints" -H "Content-Type: application/json" -H "Authorization: $TOKEN" -d "{\"cluster\":\"br1u25hw05el16h9vrmg\",\"workerpool\":\"br1u25hw05el16h9vrmg-cf5b030\",\"taints\":{\"key\":\"value1:NoSchedule\"}}"
2- Deployment which will not scale up
random_will-not-scale-scaleup.yaml
3- How to add the toleration in the POD
    a- Deployment
deployment_scaleup-1.yaml
deployment_scaleup-2.yaml
    b- Daemonset
daemonset.yaml
    c- Statefulset
statefulset.yaml
4- Scaling only configured worker pools-- By using affinity
deployment_affinity_wp-scaleup.yaml